## Slide 1: LCD Interfacing

## Slide 2: LCD Interfacing
Liquid Crystal Displays (LCDs)
cheap and easy way to display text
Various configurations (1 line by 20 X char upto 8 lines X 80 ).
Integrated controller
The display has two register
  command register
  data register
By RS you can select register
Data lines (DB7-DB0) used to transfer data and commands

## Slide 3: Alphanumeric LCD Interfacing
Pinout
  8 data pins D7:D0
  RS: Data or Command Register Select
  R/W: Read or Write
  E: Enable (Latch data)
RS – Register Select
  RS = 0  Command Register
  RS = 1  Data Register
R/W = 0  Write , R/W = 1  Read
E – Enable
  Used to latch the data present on the data pins.
D0 – D7
  Bi-directional data/command pins.
  Alphanumeric characters are sent in ASCII format.
E
R/W
RS
DB7–DB0
LCD controller
communications bus
Microcontroller
8
LCD Module

## Slide 4: LCD Working
instr ( 0x0F ) ;
data ( ‘W’ ) ;
instr ( int i ) {
RS = 1;
Enable = 1 ;
P1 = i ;
Enable = 0 ;
}
data ( int i ) {
RS = 0;
Enable = 1 ;
P1 = i ;
Enable = 0 ;
}

## Slide 5: LCD Commands
The LCD’s internal controller can accept several commands and modify the display accordingly. These commands would be things like:
  Clear screen
  Return home
  Decrement/Increment cursor
After writing to the LCD, it takes some time for it to complete its internal operations. During this time, it will not accept any new commands or data.
  We need to insert time delay between any two commands or data sent to LCD

## Slide 6: Pin Diagram
Pin No. | Name | Input / Ouput | Description
Pin no. 1 | VSS | - | Power supply (GND)
Pin no. 2 | VCC | - | Power supply (+5V)
Pin no. 3 | VEE | - | Power supply to control Contrast
Pin no. 4 | RS | Input | 0 = Instruction input 1 = Data input
Pin no. 5 | R/W | Input | 0 = Write to LCD module 1 = Read from LCD module
Pin no. 6 | EN | Input / Output | Enable signal
Pin no. 7 | D0 | Input / Output | Data bus line 0 (LSB)
Pin no. 8 | D1 | Input / Output | Data bus line 1
Pin no. 9 | D2 | Input / Output | Data bus line 2
Pin no. 10 | D3 | Input / Output | Data bus line 3
Pin no. 11 | D4 | Input / Output | Data bus line 4
Pin no. 12 | D5 | Input / Output | Data bus line 5
Pin no. 13 | D6 | Input / Output | Data bus line 6
Pin no. 14 | D7 | Input / Output | Data bus line 7 (MSB)
Pin no. 15 | Backlight | Input | +5v for LED backlight (+5V)
Pin no. 16 | Backlight | Input | Ground for LED backlight (GND)

## Slide 7: LCD Commands
Code (Decimal) | Code (Hex) | Command to LCD Instruction Register
1 | 0x01 | Clear display screen
2 | 0x02 | Return Home
4 | 0x04 | Decrement cursor (shift cursor to left)
6 | 0x05 | Increment cursor (shift cursor to right)
6 | 0x06 | shift display right
7 | 0x07 | shift display left
8 | 0x08 | Display off, cursor off
10 | 0x0A | Display off, cursor on
12 | 0x0C | Display on, cursor off
14 | 0x0E | Display on, cursor on
15 | 0x0F | Display on, cursor blinking
16 | 0x10 | Shift cursor position to left
20 | 0x14 | Shift cursor position to right
24 | 0x18 | Shift the entire display to the left
30 | 0x1C | Shift the entire display to the right
128 | 0x80 | Force cursor to the beginning of 1st line
192 | 0xC0 | Force cursor to the beginning of 2nd line
56 | 0x38 | 2 lines and 5 x 7 matrix

## Slide 8: Circuit Diagram
GND – Pin 1,3,5,16
Vcc – Pin 2, 15
+5v – Vcc
Microcontroller Pins
RS - P3.1
E – P3.2
P2